## Slide 1: Formaldehyde Training

## Slide 2: What is it used for?
Production of fertilizer
Paper
Plywood
Resins
Preservatives

## Slide 3: Health Hazards
Short term impacts via skin:
Discomfort
Minor Burns
Skin, eye, and mucus membrane irritation

## Slide 4: Inhalation Hazards
Coughing
Nausea
Vomiting
Diarrhea
Laryngitis

## Slide 5: High Concentrations
Convulsions
Coma
Death

## Slide 6: Long Term Exposure
Carcinogen and mutagen which can cause cancer

## Slide 7: Testing
Monitored by testing the air
Results are compared to OSHA’s permissible exposure limit expressed in parts per million (0.75 PPM over an 8 hour time weighted average of exposure)

## Slide 8: Short Term Testing
Based on 15 minutes of exposure (limit is no more than 2 PPM)

## Slide 9: Training
Must be annual when working with 1/10th PPM or higher which you can find on the label or safety data sheet

## Slide 10: Personal Protective Equipment
Gloves (impervious to solutions of 1% or more)
Goggles that cover entire part of eye
Face Shield
Apron
Respirator (consult SDS for correct cartridge)
Hood Vent

## Slide 11: If an incident occurs
Small spill: soak up with absorbent material or spill pillow and dispose of properly
Large spill: do not try and clean up by yourself. Vacate the area immediately and ask for help

## Slide 12: Contact with Formaldehyde
Skin: Remove infected clothing and wash area for 15 minutes
Large area of skin: Use a shower for 15 minutes and get medical attention
If eyes: Use eye wash station for 15 minutes
If swallowed: Drink water, keep warm and get medical attention
If inhaled: Go outside and call 911
Be careful when you respond. Never enter an area with high concentrations.

## Slide 13: Medical Surveillance Plan
Employee must be given a work assignment with reduced exposure until deemed able to return to work.

## Slide 14: Thank you!